## Slide 1: The Story of ChronoShare, or How NDN Brought Distributed File Sharing Back
Alex Afanasyev, Zhenkai Zhu, Yingdi Yu, Lijing Wang, and Lixia Zhang
IEEE MASS 2015 Workshop on Content-Centric Networking (CCN 2015)
October 19, 2015

## Slide 2: Introduction
File sharing is in great demand today
File synchronization models
  Centralized model
    simple implementation, but
    centralized control
    single point of failure
    delivery model mismatch
  Peer-to-peer model
    decentralized control
    no single point of failure, but
    delivery model mismatch
    underlying and p2p topology mismatch

## Slide 3: Can We Share Files in a True Distributed Way in NDN?
Name-based data retrieval
  expressed Interest for the can bring data
    from the local database, local environment (WiFi, LAN)
    from the original producer or any other user sharing the same folder
Name-based rendezvous
  Completely distributed, no need for central server
    Dedicated instance can act as backup-storage/cloud
Built-in data-oriented security
  data-oriented provenance, integrity, group-access control
Local communication is kept local
Efficient data sharing
  Multicast fashion
  “Multi-peer-to-multi-peer” file sharing
Support for device mobility and intermittent connectivity

## Slide 4: ChronoShare: Distributed File Sharing in NDN

## Slide 5: ChronoSync as a Distributed Transport Function
files, actions
knowledge
about actions
Z. Zhu and A. Afanasyev, "Let's ChronoSync: Decentralized Dataset State Synchronization in Named Data Networking," in Proceedings of the 21st IEEE International Conference on Network Protocols (ICNP 2013), Goettingen, Germany, October 2013.

## Slide 6: ChronoSync: representation of knowledge about actions
Actions
  Operation on a shared folder
  /Alice/1, /Alice/2, ...
  /Bob/1, /Bob/2, ...
  /Dave/1, /Dave/2
User’s device node
  Latest user action -> identify all actions from the user (on a device)
  /Alice/5 -> 5 actions from Alice
  /Bob/11 -> 11 actions from Bob
  /Dave/19 -> 19 actions from Dave
State digest (root digest)
  identify state of the whole shared dataset
  sha256(/Alice/5, /Bob/11, /Dave/19)
“Digest tree”

## Slide 7: ChronoShare Operations (New/Update)
/shared
/a.jpg
(v=1, c=/Alice)
Shared Folder Tree
Shared Folder Actions
/Alice/1
UPDATE /a.jpg to v=1
/Bob/1
UPDATE /a.jpg to v=2
/a.jpg
(v=2, c=/Bob)
/Dave/1
UPDATE /a.jpg to v=3
/Bob/2
UPDATE /a.jpg to v=4
/Dave/2
UPDATE /a.jpg to v=4
/a.jpg
(v=3, c=/Dave)
/a.jpg
(v=4, c=/Bob)
/a.jpg
(v=4, c=/Dave)

## Slide 8: ChronoShare Operations (Delete)
/shared
/a.jpg
(v=4, c=/Dave)
Shared Folder Tree
Shared Folder Actions
/Alice/2
UPDATE /z/b.txt to v=1
/b.txt
(v=1, c=/Alice)
/z
/Alice/3
DELETE /z/b.txt

## Slide 9: ChronoSync Digest Tree Progress
/Alice/1
UPDATE /a.jpg to v=1
/Bob/1
UPDATE /a.jpg to v=2
/Dave/1
UPDATE /a.jpg to v=3
/Bob/2
UPDATE /a.jpg to v=4
/Dave/2
UPDATE /a.jpg to v=4
/Alice/2
UPDATE /z/b.txt to v=1
/Alice/3
DELETE /z/b.txt
0x0000...
/Alice/1
/Alice/2
/Alice/3
/Bob/1
/Bob/2
/Dave/1
/Dave/2
/Alice/1
/Bob/1
/Dave/1
0xabc1...
0xbbad...
0x112a...
/Bob/2
/Dave/2
/Alice/2
/Alice/3
0x331a...
0xbbaa...
0xccaa...
Knowledge about
ChronoShare actions

## Slide 10: ChronoShare Namespaces
Separation of control/data/view namespaces
  Control namespace
    state (ChronoSync): who produced and how much data
    actions: describe produced data
      new files, file updated, file removals
  Data namespace
    files
  View namespace
    the same as file system name space
    file names as user sees them

## Slide 11: Control Namespace: State
Naming pattern
    <name-rendezvous>/<app-name>/<folder-name>/<digest>
Naming components
    <name-rendezvous>: NDN prefix to rendezvous ChronoShare participants (who will receive Sync Interests)
      /ndn/multicast
    <app-name>: one-component to demultiplex ChronoShare application interests
      ChronoShare
    <folder-name>: one-component to demultiplex ChronoShare interests for a specific shared folder
      testing4
    <digest>: root digest representing the shared folder state
Example
    /ndn/multicast/ChronoShare/testing4/109f75ca81...

## Slide 12: Control Namespace: Actions
Naming pattern
    <user’s device name>/<app-name>/ACTION/<folder-name>/<seq-no>
Naming components
    <user’s device name>: NDN prefix under which user published data on the specific device
      This is prefix under which user is authorized data publishing
      Macbook of an Alex in UCLA: /ndn/edu/ucla/alex/macbook
      Hierarchy in affiliation, not location
      Requires authorization from /ndn/edu/ucla to publish under /ndn/edu/ucla/alex prefix
    <seq-no>: number, representing sequence number of the action
Example
    /ndn/edu/ucla/alex/macbook/ChronoShare/ACTION/testing4/_seq=42

## Slide 13: Data Namespace: Files
Naming pattern
  /<user’s device name>/<app-name>/FILE/<version>/<segment>
Naming components
  <version>: version of the file produced by user’s device
  <segment>: segment number of the file (0 if file has only one segment)
Example
  /ndn/ucla.edu/zhenkai/ChornoShare/FILE/_v=1/_seg=143

## Slide 14: Advanced Operational Concepts
Each local action triggers ChronoSync sync’up
  Eventual synchronization across all devices of all users
  Remote users discover that a new action has been applied
Devices request missing action items
  All devices request the same piece of data
Action items may result in fetching new/updated file data
  Collection of action items builds a shared folder tree
Local synchronizing policies
  When and which file should be fetched
    mobile devices may want to fetch only current version
    stationary devices may fetch all the files, prioritizing the current version
  When to facilitate heterogeneous devices and connectivity
    Bluetooth, Wi-Fi, cellular

## Slide 15: Handle Mobility and Disconnects
Basic system picture
  User/device names are in general location-independent
  If a name prefix is in FIB, it is reachable, otherwise its location prefix should be in FIB
    LINK object to reach one
    the users
The focus is on getting desired data, instead of tracking device status or locations
  Find device location prefix on a “need to know” basis
  A device can report its current location prefix
How it works: focus on file, not device
  SYNC Interest brings back action data (=action+file name),
  Use file-name to fetch, if no reply, send to broadcast channel, asking “who has this file?”
  Whoever has the file replies with its location-prefix
Handle device disconnect by fetching from cached copies
A. Afanasyev, C. Yi, L. Wang, B. Zhang, and L. Zhang, "SNAMP: Secure Namespace Mapping to Scale NDN Forwarding," in Proceedings of 18th IEEE Global Internet Symposium (GI 2015), April 2015.

## Slide 16: Conclusions
ChronoSync provides universal function for distributed communication
  restrictions of ChoronoSync (per-producer sequence number) does not prohibit more complex applications to be build on top of it
  Use of an extra level of indirection
NDN with the use of ChronoSync-based ChronoShare brings back truly distributed and secure file sharing
  name-based multicast, mobile, and DTN-style data retrieval
  name-based rendezvous
  name-based communication scoping
  data-oriented security

## Slide 17: Thanks
Questions?
Email: aa@cs.ucla.edu