## Slide 1: Fuzzy Interest Forwarding
Kevin Chan (US Army Research Laboratory), Bongjun Ko (IBM T. J. Watson Research Center), Spyridon Mastorakis (UCLA), Alex Afanasyev (Florida International University), Lixia Zhang (UCLA)
Asian Internet Engineering Conference (AINTEC 2017) November 20, 2017 Bangkok, Thailand

## Slide 2: Named Data Networking
application data name
(may carry a few optional parameters)
application data name
a few pieces of metainfo
application
data
crypto signature
Data consumers send Interest packets
Whoever has the matching Data packet can reply
Publisher binds name to content; receivers verify
All data immutable
Notes: Resembles HTTP’s request/reply, with 2 important differences: data security, data immutability

## Slide 3: NDN’s node model
Content
Store
Forwarding Strategy
NDN FORWARDING DAEMON
NFD module resides in every NDN node
Pending
Interest Table
name prefix | next hop
/google/search | A, B
/fiu.edu | B,C, D
/fiu.edu/aa | A, B, D,
Multiple ways to fill FIB
Self-learning
Routing protocol
FIB
PIT breaks Interest looping, enable NDN to freely use multiple paths
Notes: CS: NDN treat storage and link the same
Forward: show multiple next hop

## Slide 4: NDN Interest Forwarding: Three Steps
Content
Store
Forwarding Strategy
NDN FORWARDING DAEMON
Pending
Interest Table
FIB
Interest
find matching name in PIT ?
2
find matching
name in CS ?
1
✔ add to PIT entry
For each PIT entry:
Interest
name
incoming
Interface(s)
outgoing interface(s)
sending time
find matching in FIB ?
3
data
✔
May forward an interest packet out through one or more interfaces
Notes: CS: talk NDN treat storage and link the same
Forward: show multiple next hop

## Slide 5: NDN Data Packet Return
Content
Store
NDN FORWARDING DAEMON
Pending
Interest Table
Interest
Interest
name
incoming
Interface(s)
outgoing interface(s)
sending time
①find a matching entry in PIT?
Eliminate DDoS by data packets
data
Calculate RTT
②
Built-in feedback loop, enable measurement
Send to all the interfaces listed here
③
Multicast data delivery
④save in content store
caching
④ remove the PIT entry
5
Notes: Data comes back: show potential multicast; NOTE Interests are forwarded, data traverses exactly the same path Interest laid the state, create a feedback loop. Cache freshness controlled by data producer

## Slide 6: Forwarding Strategy
Forwarding Strategy makes interest forwarding decisions by taking input from
  FIB
  measurement from Interest-data exchange (and any other local resource information)
  Per-namespace forwarding policies
A hook to control plane
FIB
Content
Store
Pending Interest
Table (PIT)
Forwarding strategy
NDN FORWARDING DAEMON
Routing
protocol
Notes: Even with a control plane, Best approach is NOT to repalce the routing protocol, let it reflect true connectivity status

## Slide 7: Steering Interests Toward Matching Data
DATA
Origin
data source
Processing
unit
INTEREST
Data source, storage, and processing units can all supply requested data
With no prior knowledge: may try broadcast discovery, or even random walk
Building knowledge of directions to reach data: routing announcement
opportunistic caching
stable
storage (repo)
Interest packets are forwarded and matched with data using hierarchical names or prefixes
Notes: Random walk: NDN can keep the memory of failed paths

## Slide 8: How Consumers Discover Data Names or Prefixes
Search engines
Naming conventions
  /park/yellowstone/alerts
    Retrieves the latest version of known alerts
      => /park/yellowstone/alerts /_v=2017-11-17
      => /park/yellowstone/alerts /_v=2017-04-18
      => /park/yellowstone/alerts /_v=2017-04-19
Metadata
  /park/_nodes
    { yellowstone }
  /park/yellowstone/_nodes
    { alerts }
Require access to infrastructure and/or multiple Interest/Data exchanges

## Slide 9: Efficient Data Discovery in Challenging Environments
/park/yellowstone/lost&found/dog/…
/park/yellowstone/lost&found/pup/…
/park/yellowstone/lost&found/canine/…

## Slide 10: Fuzzy Interest Forwarding Extension
Content
Store
Forwarding Strategy
NDN FORWARDING DAEMON
Pending
Interest Table
FIB
Interest
data
✔
Fuzzy
Lookup
Fuzzy
Lookup
/park/yellowstone/lost&found/
/park/yellowstone/lost&found/
/park/yellowstone/lost&found/
/park/yellowstone/lost&found/?pet?
Notes: CS: talk NDN treat storage and link the same
Forward: show multiple next hop

## Slide 11: Ontological Matching
Predefined name ontology given by a lexical database
Feasible when matching in resource-rich computing nodes
Source
  UCI Zoo dataset, WordNet corpus, WUP Similarity Function
Large database
Expensive lookup
Suitable only for resource-rich nodes

## Slide 12: Contextual Matching
Construct a vector space model for contextual similarity distance between words/names
  Mapping function learned from a corpus of texts
  Names in CS and FIB are mapped to vectors
  A (part of) Interest name mapped to a vector
  Semantically similar names are found in the vector space
Source
  Prefix announcements
  Static corpuses of texts
Approximate nearest neighbor search
  Locality Sensitive Hashing (LSH): O(1) O(log n) lookup time
Could be feasible for constrained devices

## Slide 13: Estimated Performance of Approximate Nearest Neighbor Search

## Slide 14: Fuzzy Match of the Hierarchical Name
Exact match on a prefix
  Disambiguate context of the requested data
    /park/yellowstone/lost&found
    /news/cnn
Fuzzy match of a single name component
Fuzzy match on multiple components
  Independently on each component
  Considering components as a “sentence”
    …/animal/dog/…
    …/being/mammal/…

## Slide 15: Implementation in ndnSIM
Comparison of FIF with Exact Match Forwarding (EMF)
Word2vec requires 98MB (71K words) -> 1.2 GB (3M) for dictionaries
Data retrieval rate: FIF slower than EMF
  4 times slower for small FIB sizes, 5.2 slower for large FIB sizes

## Slide 16: Identified Challenges
Resource Constraints
  added computation and storage expense for semantic matching
Require feedback of fuzzy matching
  NACK and/or relevant names/ name prefixes
Potential attack surface
  detection of false data injection

## Slide 17: Thanks!