## Slide 1: Internet-of-Things (IoT)
Summer Engineering Program 2018
University of Notre Dame

## Slide 2: Course Overview
 | Lecture | Lab
Week 1 | Fundamentals of IoT, basic concepts, applications | Basic Python & Raspberry Pi programming
Week 2 | Human-computer interfaces, sensing, actuation | Sensor programming, control loops, digital/analog I/O
Week 3 | Fundamentals of computer and wireless networks | Wi-Fi and Bluetooth networks, network measurements
Week 4 | Sensor networks, mesh networks, routing, WPANs | ZigBee, WPANs, WBANs, routing, network measurements
Week 5 | Processing, IoT cloud, analytics, visualization | IoT cloud integration, sensor fusion, analytics, visualization
Week 6 | RFID, IoT ecosystem, security, privacy, ethics, case studies | Final project

## Slide 3: Components of an IoT Device

## Slide 4: Embedded System/Computer
“Any sort of device which includes a programmable computer but itself is not intended to be a general-purpose computer”
      Wayne Wolf
General purpose
Dedicated

## Slide 5: Automotive Embedded Systems

## Slide 6: Automotive Embedded Systems
Today’s high-end automobile may have 100+ microprocessors:
  Seat belt; dashboard devices; engine control; ABS; automatic stability control; navigation system; infotainment system; collision avoidance system; tire pressure monitoring; lane warning; adaptive cruise control; climate control; airbag control unit; electric window and central locking; parking aid; automatic wiper control; alarm and immobilizer; power seat; electric power steering; electronic transmission; active suspension

## Slide 7: Embedded Processor Market
80 million PCs every year
3 billion embedded CPUs every year
Embedded systems market growing, while PC market mostly saturated

## Slide 8: General-Purpose Processor
Programmable device, “microprocessor”
Features
  Program memory
  General data path with large register file and general ALU
User benefits
  Low time-to-market and NRE costs
  High flexibility
Examples: Intel Core i7, AMD Ryzen 5, etc.
IR
PC
Register
file
General
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory

## Slide 9: Dedicated Processor
Digital circuit designed specifically for one purpose
Features
  Contains only the components needed to execute a single program
  No program memory
Benefits
  Fast
  Low power
  Small size
Datapath
Controller
Control logic
State register
Data
memory
index
total
+

## Slide 10: Application-Specific Processor (ASIC)
Programmable processor optimized for a particular class of applications that have common characteristics (compromise)
Features
  Program memory
  Optimized data path
  Special functional units
Benefits
  Some flexibility, good performance, size, and power, “reusable”
IR
PC
Registers
Custom
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory

## Slide 11: Characteristics of Embedded Systems
Dedicated functionality
Real-time operation
Small size and low weight
Low power
Harsh environments
Safety-critical operation
Cost sensitive

## Slide 12: Embedded vs. Real Time Systems
Embedded system: is a computer system that performs a limited set of specific functions; it often interacts with its environment
RTS: Correctness of the system depends not only on the logical results, but also on the time in which the results are produced
Embedded
Systems
Real Time
Systems
Examples?

## Slide 13: Examples
Real Time Embedded:
  Nuclear reactor control
  Flight control
  Basically any safety critical system
  GPS
  MP3 player
  Mobile phone
Real Time, but not Embedded:
  Stock trading system
  Skype
  Pandora, Netflix
Embedded, but not Real Time:
  Home temperature control
  Sprinkler system
  Washing machine, refrigerator, etc.

## Slide 14: Characteristics of RTS
Event-driven (reactive) vs. time-driven
Reliability/fault-tolerance requirements (example: triple modular redundancy)
Predictability
Priorities in multi-programmed systems

## Slide 15: Taxonomy
Hard RT: absolutely imperative to meet all timing constraints
Soft RT: deadlines are important, but the system will still function even if deadline is missed Firm RT: no value, but not catastrophic

## Slide 16: Taxonomy: Static
Task arrival times can be predicted
Static (compile-time) analysis possible
Allows good resource usage (low idle time for processors)

## Slide 17: Taxonomy: Dynamic
Arrival times unpredictable
Static (compile-time) analysis possible only for simple cases
Processor utilization varies dramatically; must design system to handle “worst case”
Must avoid over-simplifying assumptions
  e.g., assuming that all tasks are independent, when this is unlikely

## Slide 18: Taxonomy: Periodic
Each task (or group of tasks) executes repeatedly with a particular period
Allows some static analysis techniques to be used
Matches characteristics of many real problems
It is possible to have tasks with deadlines smaller, equal to, or greater than their period
  the later are difficult to handle (i.e., multiple concurrent task instances occur)

## Slide 19: Taxonomy: Periodic
Single rate:
  One period in the system
  Simple but inflexible
  Used in implementing a lot of wireless sensor networks
Multi rate:
  Multiple periods
  Should be harmonics to simplify system design

## Slide 20: Taxonomy: Aperiodic
Are also called sporadic, asynchronous, or reactive
Creates a dynamic situation
Bounded arrival time intervals are easier to handle
Unbounded arrival time intervals are impossible to handle with resource-constrained systems

## Slide 21: Control Systems
Man-machine interface: input devices, e.g., keyboard and output devices, e.g., display
Instrumentation interface: sensors and actuators that transform between physical signals and digital data
Most control systems are hard real-time
Deadlines are determined by the controlled object, i.e., the temporal behavior of the physical phenomenon (fuel injection vs. ATM)
Operator
Controlled Object
Real-Time Computer System
Man-Machine
Interface
Instrumentation
Interface

## Slide 22: Control System Example
Example: A simple one-sensor, one-actuator control system.
control-law
computation
A/D
A/D
D/A
sensor
plant
actuator
rk
yk
y(t)
u(t)
uk
reference
input r(t)
The system
being controlled
Outside effects

## Slide 23: Control Systems Cont’d.
Pseudo-code for this system:
set timer to interrupt periodically with period T;
at each timer interrupt do
do analog-to-digital conversion to get y;
compute control output u;
output u and do digital-to-analog conversion;
end do
T is called the sampling period. T is a key design choice. Typical
range for T: seconds to milliseconds.

## Slide 24: Sensors and Actuators
Sensors:
  They are mainly input components
  They sense and collect surrounding information
Actuators:
  They are mainly output components
  They alter the surrounding

## Slide 25: Communications
Connects devices with each other & the cloud
Communication type:
  Wireline (e.g., copper wires, optical fibers)
  Wireless (e.g., RF, IR); RF-based communication is the most popular choice
Popular RF-based communication solutions:
  IEEE 802.15.4
  IEEE 802.11 (or Wifi)
  Bluetooth
  Near Field Communication (NFC), e.g., RFID

## Slide 26: Components of an IoT Device
IoT EcoSystem
Weeks 5&6
Week 1
Week 1
Week 2
Week 2
Weeks 3&4

## Slide 27: BREAK