## Slide 1: Internet-of-Things (IoT)
Summer Engineering Program 2018
University of Notre Dame

## Slide 2: Course Overview
 | Lecture | Lab
Week 1 | Fundamentals of IoT, basic concepts, applications | Basic Python & Raspberry Pi programming
Week 2 | Human-computer interfaces, sensing, actuation | Sensor programming, control loops, digital/analog I/O
Week 3 | Fundamentals of computer and wireless networks | Wi-Fi and Bluetooth networks, network measurements
Week 4 | Sensor networks, mesh networks, routing, WPANs | ZigBee, WPANs, WBANs, routing, network measurements
Week 5 | Processing, IoT cloud, analytics, visualization | IoT cloud integration, sensor fusion, analytics, visualization
Week 6 | RFID, IoT ecosystem, security, privacy, ethics, case studies | Final project

## Slide 3: Sensors
A sensor is a device that receives a stimulus and responds with an electrical signal.

## Slide 4: Computer Process Control System
Actuators
Computer
Controller
Transformation Process
Sensors
DAC
ADC
Input Devices
Output Devices
Continuous and Discrete
Variables
Continuous and Discrete
Parameters

## Slide 5: What is a Stimulus?
Motion, position, displacement
Velocity and acceleration
Force, strain
Pressure
Flow
Sound
Moisture
Light
Radiation
Temperature
Chemical presence
Visual Sensor
Ultrasound Sensor
Infrared Sensor

## Slide 6: What is a Response?
When we say electrical we mean a signal which can be channeled, amplified, and modified by electronic devices:
  Voltage
  Current
  Charge

## Slide 7: Sensor as Energy Converter
This conversion can be direct or it may require transducers
Example:
  A chemical sensor may have a part which converts the energy of a chemical reaction into heat (transducer) and another part, a thermopile, which converts heat into an electrical signal

## Slide 8: Physical Principles of Sensing
Charges, fields, & potentials
Capacitance
Magnetism
Induction
Resistance
Piezoelectric effect
Seebeck and Peltier effects
Thermal properties of materials
Heat transfer
Light

## Slide 9: Capacitance
Two isolated conductive objects of arbitrary shape, which can hold an electric charge, are called a capacitor
  An electric field is developed between the two conductors

## Slide 10: Capacitor as Displacement Sensor
If the inner conductor can be moved in and out, the measured capacitance will be a function of l

## Slide 11: Dielectric Constant
The material between the plates of the capacitor can also be used to sense changes in the environment.
  When vacuum (or air) is replaced by another material, the capacitance increases by a factor of , known as the dielectric constant of the material
  The increase in C is due to the polarization of the molecules of the material used as an insulator

## Slide 12: Example – A Water Level Sensor
The total capacitance of the coaxial sensor shown below is the capacitance of the water-free portion plus the capacitance of the water-filled portion; as the level of the water changes, the total capacitance changes

## Slide 13: Magnetism
There are two methods of generating a magnetic field:
  permanent magnets (magnetic materials)
  magnetic field generated by a current
Force is generated on a test magnet in the field of magnetic materials.
A compass needle will respond to the magnetic field generated by a current.
Magnetic field, B
“flux” is the field density, B

## Slide 14: Sources of Magnetic Fields
Electric current sets a circular magnetic field around a conductor.
Moving electron sets a field, superposition of field vectors results in a combined magnetic field of a permanent magnet.
Magnets are useful for fabricating magnetic sensors for the detection of motion, displacement, and position.

## Slide 15: Induction
A phenomenon related to magnetism is induction, the generation of voltage from a changing magnetic field
  If the coil has no magnetic core, the flux is proportional to current and the voltage proportional to di/dt

## Slide 16: Resistance
If we apply a battery across two points of a piece of material, an electric field will be set up where E=V/l
The tendency of the material to resist the flow of electrons is called its resistivity, , and we say that the material has a particular electrical resistance, R.

## Slide 17: Sensitivity of Resistance
To Temperature:
Specific resistivity of tungsten as a function of temperature.
 is the temperature coefficient of resistivity.

## Slide 18: The Piezoelectric Effect
The piezoelectric effect is the generation of electric charge by a crystalline material upon subjecting it to stress

## Slide 19: Piezoelectric Sensor
Piezoelectric crystals are direct converters of mechanical energy into electrical energy.
Because a crystal with deposited electrodes forms a capacitor the voltage developed can be expressed as:
Where dx is the piezoelectric coefficient in the x direction and Fx is the applied force in the x direction.
Laminated 2-layer piezoelectric sensor

## Slide 20: Signal Conditioning
Filter for expected frequency regime
Subtract DC offset (“zeroing”)
Amplify or attenuate signal (“scaling”)
Linearize relationship between measured and observed electrical parameter
Analog-to-Digital (and Digital-to-Analog) conversion

## Slide 21: Analog-to-Digital Conversion
Sampling – converts the continuous signal into a series of discrete analog signals at periodic intervals
Quantization – each discrete analog is converted into one of a finite number of (previously defined) discrete amplitude levels
Encoding – discrete amplitude levels are converted into digital code
Variable
Time
Analog Signal
1001
1101
0101
Discrete
Variables

## Slide 22: Features of an ADC
Sampling rate – rate at which continuous analog signal is polled (e.g., 1000 samples/sec)
Quantization – divide analog signal into discrete levels
Resolution – depends on number of quantization levels
Conversion time – how long it takes to convert the sampled signal to digital code
Conversion method – means by which analog signal is encoded into digital equivalent
  Example: Successive approximation method

## Slide 23: Successive Approximation Method
A series of trial voltages are successively compared to the input signal whose value is unknown
Number of trial voltages = number of bits used to encode the signal
First trial voltage is 1/2 the full scale range of the ADC
If the remainder of the input voltage exceeds the trial voltage, then a bit value of 1 is entered, if less than trial voltage then a bit value of zero is entered
The successive bit values, multiplied by their respective trial voltages and added, becomes the encoded value of the input signal

## Slide 24: Example
Analogue signal is 6.8 volts. Encode, using SAM, the signal for a 6 bit register with a full scale range of 10 volts.

## Slide 25: Example
Q = resolution in volts per step
M = resolution in bits
N = Number of intervals (steps, quantization levels)
EFSR = Full scale voltage range
Quantization error = ½ of interval
Voltage range 0 – 10V; M = 12 bits
N = 4096 intervals (steps)
Q = 2.44 mV/code

## Slide 26: Example
Using an analogue-to-digital converter, a continuous voltage signal is to be converted into its digital counterpart. The ADC has a 16-bit capacity, and full scale range of 60 V. Determine:
  number of quantization levels
  resolution
  quantization error

## Slide 27: Solution
(1) Number of quantization levels:
= 216 = 65,536
(2) Resolution:
= 60 / 65,536 = ~ 0.00092 Volts
(3) Quantization error:
= 0.00092/2 = 0.00046 Volts

## Slide 28: Digital-to-Analog Conversion
Convert digital values into continuous analogue signal
  Decoding digital value to an analogue value at discrete moments in time based on value within register
  Where E0 is output voltage; Eref is reference voltage; Bn is status of successive bits in the binary register

## Slide 29: Example
A DAC has a reference voltage of 100 V and has 6-bit precision. Three successive sampling instances 0.5 sec apart have the following data in the data register:
Output Values:
Instant Binary Data
1 101000
2 101010
3 101101
E01 = 100{0.5(1)+0.25(0)+0.125(1)+0.0625(0)+0.03125(0)+0.015625(0)}
E01 = 62.50V
E02 = 100{0.5(1)+0.25(0)+0.125(1)+0.0625(0)+0.03125(0)+0.015625(0)}
E02 = 65.63V
E03 = 100{0.5(1)+0.25(0)+0.125(1)+0.0625(0)+0.03125(0)+0.015625(0)}
E03 = 70.31V

## Slide 30: Sensor Types: HW & SW
Hardware-based sensors
  Physical components built into a device
  They derive their data by directly measuring specific environmental properties
Software-based sensors
  Not physical devices, although they mimic hardware-based sensors
  They derive their data from one or more hardware-based sensors

## Slide 31: Sensor List of Smartphones
Sensor | Function Type | Software-based or Hardware-based
Accelerometer | Motion Sensor | Hardware-based
Gyroscope | Motion Sensor | Hardware-based
Gravity | Motion Sensor | Software-based
Rotation Vector | Motion Sensor | Software-based
Magnetic Field | Position Sensor | Hardware-based
Proximity | Position Sensor | Hardware-based
GPS | Position Sensor | Hardware-based
Orientation | Position Sensor | Software-based
Light | Environmental Sensor | Hardware-based
Thermometer | Environmental Sensor | Hardware-based
Barometer | Environmental Sensor | Hardware-based
Humidity | Environmental Sensor | Hardware-based

## Slide 32: Sensor: Motion and Orientation
Most of the sensors use the same coordinate system
When a device’s screen is facing the user
  The X axis is horizontal and points to the right
  The Y axis is vertical and points up
  The Z axis pints toward outside of the screen face

## Slide 33: Sensor: Accelerometer
Measure proper acceleration (acceleration it experiences relative to free fall)
Units: g

## Slide 34: Sensor: Accelerometer
Acceleration is measured on 3 axes
Note that the force of gravity is always included in the measured acceleration
  When the device is sitting on the table stationary, the accelerometer reads a magnitude of 1g
  When the device is in free fall, the accelerometer reads a magnitude of 0g
To measure the real acceleration of the device, the contribution of the force of gravity must be removed from the reading, for example, by calibration

## Slide 35: Sensor: Accelerometer
When the device is lying flat
  gives +1g (gravitational force) reading on Z axis
Stationary device, after 45 degree rotation
  Same magnitude, but rotated

## Slide 36: Accelerometer: Inner Working (1 of 2)
It consists of beams and a capacitive sensor with some anchor points

## Slide 37: Accelerometer: Inner Working (1 of 2)
On applying the acceleration, the beams deflect and cause the change in capacitance.

## Slide 38: Accelerometer
Mass on spring
Gravity
Free Fall
Linear Acceleration
Linear Acceleration plus gravity
1g = 9.8m/s2
-1g
1g

## Slide 39: Smartphones: MEMS Sensors
Micro Electro-Mechanical Systems
Term coined in 1989
Describes creation of mechanical elements at a scale more usually reserved for microelectronics
MEMS use cavities, channels, cantilevers, membranes, etc. to imitate traditional mechanical systems
Small enough to be integrated with the electronics

## Slide 40: MEMS Accelerometer

## Slide 41: MEMS Accelerometer
Have a proof mass between springs and a series of ‘plates’
Measure deflection via capacitance changes
1-D only

## Slide 42: Sensor: Gravity
Gravity sensor is not a separate hardware
It is a virtual sensor based on the accelerometer
It is the result when real acceleration component is removed from the reading

## Slide 43: Sensor: Gyroscope
Measures the rate of rotation (angular speed) around an axis
Speed is expressed in rad/s on 3 axis
When the device is not rotating, the sensor values will be zeros
It gives us 3 values
  Pitch value (rotation around X axis)
  Roll value (rotation around Y axis)
  Yaw value (rotation around Z axis)
Gyroscope is error prone over time
As time goes, gyroscope introduces drift in result
By sensor fusion (combining accelerometer and gyroscope), results can be corrected and path of movement of device can be obtained correctly

## Slide 44: Gyroscope
Normally, a drive arm vibrates in a certain direction.
Direction of rotation
When the gyro is rotated, the Coriolis force acts on the drive arms, producing vertical vibration.
The stationary part bends due to vertical drive arm vibration, producing a sensing motion in the sensing arms.
The motion of a pair of sensing arms produces a potential difference from which angular velocity is sensed. The angular velocity is converted to, and output as, an electrical signal.

## Slide 45: MEMS Gyroscope
Based on measuring Coriolis force as experienced by a moving object in a rotating frame of reference
Many implementations, but the “tuning fork” method is most common

## Slide 46: Accelerometer vs. Gyroscope
Accelerometer
  Senses linear movement: not good for rotations, good for tilt detection
  Does not know difference between gravity and linear movement
Gyroscope
  Measures all types of rotations
  Not movement
A+G = both rotation and movement tracking possible

## Slide 47: Sensor: Magnetic Field
Measures direction and strength of earth’s magnetic field
Strength is expressed in tesla (T)

## Slide 48: Compass
Magnetic field sensor (magnetometer)
Z
X
Y
X
Y
Z
Magnetic inclination
Horizontal
Gravity
Magnetic field vector
Magnetic declination
Magnetic north
Geographic north

## Slide 49: MEMS Compass
Most use Lorentz Force
A current-carrying wire in a magnetic field experiences a perpendicular force

## Slide 50: Actuators
Hardware devices that convert a controller command signal into a change in a physical parameter
  The change is usually mechanical (e.g., position or velocity)
  An actuator is also a transducer because it changes one type of physical quantity into some alternative form
  An actuator is usually activated by a low-level command signal, so an amplifier may be required to provide sufficient power to drive the actuator

## Slide 51: Types of Actuators
Electrical actuators
  Electric motors
    DC servomotors
    AC motors
    Stepper motors
  Solenoids
Hydraulic actuators
  Use hydraulic fluid to amplify the controller command signal
Pneumatic actuators
  Use compressed air as the driving force