## Slide 1: Internet-of-Things (IoT)
Summer Engineering Program 2018
University of Notre Dame
LAB COMPONENT

## Slide 2: Office Hours Reminders & Notes
1 hour before class Mon/Wed and leaving last after class; Fri 9-10.30 (up to 12pm if needed) + Jess‘ office hours
First always try to solve a problem yourself (Google is your friend!)
If stuck, isolate problem (print is your friend!)
Come with specific questions (colleagues, TA, and Prof are your friends!)
  Keep in mind we have 26 students; if everybody „consumes“ 1 hour of Jess‘ time, that won‘t work out
  „Collaborate“ versus „tutoring“
Do not delay!!! (time is not your friend!)
Keep copies of your code!

## Slide 3: Bluetooth
Basic idea
  Universal radio interface for ad-hoc wireless connectivity
  Interconnecting computer and peripherals, handheld devices, PDAs, cell phones – replacement of IrDA (Infrared Data Association)
  Embedded in other devices, very cheap
  Short range (10m), low power consumption, license-free 2.45 GHz ISM
  Voice and data transmission

## Slide 4: Bluetooth
History
  1994: Ericsson worked on “MC-link” project
  Later renamed to Bluetooth: Harald “Blåtand” Gormsen [son of Gorm], King of Denmark in the 10th century; united Denmark and spread Christianity
  1998: foundation of Bluetooth SIG (Special Interest Group): www.bluetooth.org
  2001: first consumer products for mass market, spec. version 1.1 released
  2005: 250 million chips
  2018: 4 billion chips

## Slide 5: Key Characteristics
2.4 GHz ISM band, 79 RF channels
  Channel 0: 2402 MHz … channel 78: 2480 MHz
Frequency hopping
  1600 hops/s
  Hopping sequence in a pseudo random fashion, determined by a master
Two types of traffic:
  Voice link – SCO (Synchronous Connection Oriented)
  Data link – ACL (Asynchronous Connection Less)

## Slide 6: Topology: Piconet & Scatternet

## Slide 7: Bluetooth Piconet
Master gives slaves its clock and device ID
  Hopping pattern: determined by device ID (48 bit, unique worldwide)
  Pseudo random number generator (device ID + clock)
Addressing
  Active Member Address (AMA, 3 bit)
  Parked Member Address (PMA, 8 bit)
  Standby Member (no address)
M=Master
S=Slave
P=Parked
SB=Standby
M
S
P
SB
S
S
P
P
SB










## Slide 8: Bluetooth Scatternet
Each piconet has one master, but slaves can participate in different piconets on a time-division multiplex basis
A master in one piconet can be a slave in other piconets
Each piconet has its own hopping sequence

## Slide 9: Bluetooth Scatternet
M=Master
S=Slave
P=Parked
SB=Standby
M
S
P
SB
S
S
P
P
SB
M
S
S
P
SB
Piconets

## Slide 10: Communication
S
fk
625 µs
fk+1
fk+2
fk+3
fk+4
fk+3
fk+4
fk
fk
fk+5
fk+5
fk+1
fk+6
fk+6
fk+6
M
M
M
M
M
M
M
M
M
t
t
t
S
S
S
S
S

## Slide 11: Communication Example
Polling-based time division multiplex
  625µs slots, master polls slaves
SCO (Synchronous Connection Oriented) – Voice
ACL (Asynchronous ConnectionLess) – Data
  Variable packet size (1, 3, 5 slots)
MASTER
SLAVE 1
SLAVE 2
f6
f0
f1
f7
f12
f13
f19
f18
SCO
SCO
SCO
SCO
ACL
f5
f21
f4
f20
ACL
ACL
f8
f9
f17
f14
ACL

## Slide 12: Bluetooth Versions

## Slide 13: Bluetooth Low Energy (BLE)
Bluetooth low energy is a new, open, short range radio technology
  Blank sheet of paper design
  Different to Bluetooth classic
  Optimized for ultra low power
  Enable coin cell battery use cases
    < 20mA peak current
    < 5uA average current

## Slide 14: BLE Basic Concepts
Everything is optimized for lowest power consumption
  Short packets reduce TX (transmit) peak current
  Short packets reduce RX (receive) time
  Fewer RF channels to improve discovery and connection time
  Simple state machine
  Single protocol
  ...

## Slide 15: “Exposing State” (IoT)
It’s good at small, discrete data transfers
Data can triggered by local events
Data can be read at any time by a client
23.2˚C
Gate 10 BOARDING
12:23 pm
60.5 km/h
3.2 kWh
PLAY >>
Network Available

## Slide 16: BLE Device Modes
Dual Mode
  Bluetooth Classic and LE
  Used anywhere BT Classic is used today
Single Mode
  Implements only Bluetooth low energy
  Will be used in new devices / applications

## Slide 17: BLE Physical Layer
2.4 GHz ISM band
40 Channels on 2 MHz spacing

## Slide 18: BLE Physical Layer
Two types of channels

## Slide 19: BLE Physical Layer
Advertising channels avoid 802.11

## Slide 20: BLE Link Layer
Link Layer state machine

## Slide 21: BLE and Internet-of-Things
My pulse is …
My blood glucose is …
My temperature is …
Low power
Low data rate

## Slide 22: Assignment 3
Task 1: Configure Bluetooth
Task 2: Write a client-server based intruder detection system using 2 Pis, a PIR sensor, and an LED (and/or sounder)
  One Pi acts as server and uses a callback function that triggers when motion is detected
  The other Pi acts as client and queries the server for the PIR value once every 5 seconds; if an intrusion is detected, the alarm is raised
  Test both your client AND server program with the help of one (or more) of your classmates

## Slide 23: Assignment 3 Deliverables
By Friday midnight submit a report showing clearly your client and server programs
Indicate your Bluetooth address
Indicate if you ran into any problems during development or if any parts are incomplete/etc.
Provide a brief video (no longer than 30 seconds each) that shows your Pi and your classmate‘s Pi work together as intrusion detection system
Summary: there are two documents for this assignment: one PDF report (with code) and one video

## Slide 24: Bluetooth Preparation
Make sure Internet sharing is w0rking (e.g., ping a remote IP address)
Install the Bluez Bluetooth module on your Pi:
  sudo apt-get update
  sudo apt-get install python-bluez
Configure Bluetooth:
  sudo bluetoothctl
    type: agent on
    type: default-agent
    type: scan on
    type: quit
Activate scanning:
  sudo hciconfig hci0 piscan
  This call needs to be done after each reboot of the Pi!
If needed, you can find your Pi‘s BT address using the following command:
  hciconfig (the address format is: XX:XX:XX:XX:XX:XX)

## Slide 25: Bluetooth Server Template
import bluetooth
hostMACAddress = ''
port = 3
backlog = 1
size = 1024
s = bluetooth.BluetoothSocket(bluetooth.RFCOMM)
s.bind((hostMACAddress, port))
s.listen(backlog)
try:
client, clientInfo = s.accept()
while 1:
data = client.recv(size)
if data:
print(data)
client.send("Returning: " + data)
except:
client.close()
s.close()

## Slide 26: Bluetooth Client Template
import bluetooth
serverMACAddress = ‘XX:XX:XX:XX:XX:XX'
port = 3
size = 1024
s = bluetooth.BluetoothSocket(bluetooth.RFCOMM)
s.connect((serverMACAddress, port))
while 1:
text = raw_input("Text to send: ")
if text == "quit":
break
s.send(text)
data = s.recv(size)
print(data)
s.close()

## Slide 27: Notes
The client specifies the address of the server
The server specifies an empty address (the server will find its BT adapter address by itself)
The port number can be changed, but must be the same in both client & server
The size value indicates the maximum size of a data transfer

## Slide 28: Client/Server Communication