## Slide 1: Internet-of-Things (IoT)
Summer Engineering Program 2018
University of Notre Dame

## Slide 2: Course Overview
 | Lecture | Lab
Week 1 | Fundamentals of IoT, basic concepts, applications | Basic Python programming, meet your Raspberry Pi
Week 2 | Smart objects, user interfaces, sensing, actuation | Sensor programming, control loops, digital/analog I/O
Week 3 | Fundamentals of computer and wireless networks | Wi-Fi and Bluetooth networks, network measurements
Week 4 | Sensor networks, mesh networks, routing, WPANs | ZigBee, WPANs, WBANs, routing, network measurements
Week 5 | Processing, IoT cloud, analytics, visualization | IoT cloud integration, sensor fusion, analytics, visualization
Week 6 | IoT ecosystem, security, privacy, ethics, trends, case studies | Final project

## Slide 3: Review Munich
IBM speaker
  INTELLIGENT IoT (collaboration, conversational interfaces, slow/focused introduction of technology)
Samsung speaker
  In-memory analysis; “imprecise computation“
Uppsala speaker
  Inter-network interaction; co-locality of networks
USC speaker
  IoT marketplace; sharing of data

## Slide 4: Review Munich
Vint Cerf (Google)
  Reliability, safety, security, privacy, interoperability, autonomy, …
Panel
  Closed vs. open approach
Data:Lab Munich
  Connected vehicles; data science; quantum computing; natural language processing
  SDK (Software Development Kit), API (Application Programming Interface)

## Slide 5: Review Munich
Prof. Barker
  SWAG
  Circuit-switched vs. packet-switched
  Packet drop (routers)
  Real-time focus
  System on a chip (SoC)
  State machines
  Virtual memory
  RPC (remote procedure call)
  IPv4 vs. IPv6
  Object-oriented vs. predictability
  6LowPan

## Slide 6: Computer Network Terminology
Network: group of computers and associated devices that are connected by communication facilities
Wide Area Network (WAN): world-wide (Internet)
Metropolitan Area Network (MAN): city-scale
Local Area Network (LAN): laboratory/office-scale (Ethernet)
  WLAN: wireless LAN (Wi-Fi)
  WPAN: wireless personal area network (Bluetooth)
  WBAN: wireless body area network

## Slide 7: Network Topologies

## Slide 8: Network Protocols
Protocols are the building blocks of a network architecture
Formal standards and policies enabling communication
IEEE (Institute of Electrical and Electronics Engineers): standardization
  Example: Project 802
    802.3: Ethernet
    802.11: WLAN
    802.15: WPAN

## Slide 9: Communication
Who initiates communication?
Order of communication?
How long can I talk?
How loud can I speak?
Do I have to say something specific at beginning or end?
Do I have to add meta information?
What do I do if I get interrupted?
What do I do if I was not understood?

## Slide 10: Protocols
Hi
Hi
Got the
time?
2:00
TCP connection
request
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time

## Slide 11: Client/Server Model
Client: “active” (initiates communication)
Server: “passive” (listens and responds)

## Slide 12: Client/Server Model Examples
HTTP (Hypertext Transfer Protocol)
SMTP (Simple Mail Transfer Protocol)
SSH (Secure Shell)
DNS (Domain Name System)
NFS/AFS (Network/Andrew File System)

## Slide 13: Network Protocols (“Protocol Stack”)
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Communication Network
Figure 2.6
Copyright ©2000 The McGraw Hill Companies

## Slide 14: Network Protocols (Headers/Trailers)
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application A
Application B
data
data
data
data
data
data
data
ah
ph
sh
th
nh
dh
bits
dt

## Slide 15: Why A Layered Design?
An explicit structure for dealing with a complex system
Simplifies the design process
Modularity of layers eases maintenance and updating of system components
Accommodates incremental changes

## Slide 16: Open System Interconnection (OSI)

## Slide 17: Physical Layer (Layer 1)
Physical/electrical characteristics
Cable type, length, connectors, voltage levels, signal durations, ...
Binary data (bits) as electrical or optical signals
Frequencies (wireless)

## Slide 18: Wireless Characteristics
VLF = Very Low Frequency UHF = Ultra High Frequency
LF = Low Frequency SHF = Super High Frequency
MF = Medium Frequency EHF = Extra High Frequency
HF = High Frequency UV = Ultraviolet Light
VHF = Very High Frequency
Frequency and wave length
   = c/f
  wave length , speed of light c  3x108m/s, frequency f
1 Mm
300 Hz
10 km
30 kHz
100 m
3 MHz
1 m
300 MHz
10 mm
30 GHz
100 m
3 THz
1 m
300 THz
visible light
VLF
LF
MF
HF
VHF
UHF
SHF
EHF
infrared
UV

## Slide 19: Frequencies for Mobile Communication
Low Frequencies:
  low data rates
  travel long distances
  follow Earth’s surface
  penetrate objects and water (submarine communication)
High Frequencies:
  high data rates
  short distances
  straight lines
  cannot penetrate objects (“Line of Sight” or LOS)

## Slide 20: Other Propagation Effects
Shadowing
Reflection at large obstacles
Refraction depending on the density of a medium
Scattering at small obstacles
Diffraction at edges
reflection
scattering
diffraction
shadowing
refraction

## Slide 21: Real World Examples

## Slide 22: Multipath Propagation
Signal can take many different paths between sender and receiver due to reflection, scattering, diffraction
signal at sender
signal at receiver
LOS pulses
multipath
pulses
Delay Spread

## Slide 23: Digital Modulation
Amplitude Shift Keying (ASK):
  very simple
  low bandwidth requirements
  very susceptible to interference
Frequency Shift Keying (FSK):
  needs larger bandwidth
Phase Shift Keying (PSK):
  more complex
  robust against interference
1
0
1
t
1
0
1
t
1
0
1
t

## Slide 24: Data Link Layer (Layer 2)
Defines when/how medium will be accessed for transmission
Units typically called “frames”; error detection/correction; divided into sublayers, including: MAC = Medium Access Control (MAC address 6f:00:2b:23:1f:32)
Cell phone example:

## Slide 25: Example: Ethernet (802.3)
Most popular LAN technology, uses bus architecture
Easy to install, inexpensive
Data is broken into packets

## Slide 26: Example: Ethernet
Medium Access Control (MAC) protocol
CSMA/CD Protocol
  Carrier Sense
  Multiple Access
  Collision Detection
A
C
B
collision

## Slide 27: Example: Ethernet
“Sense” (listen) carrier (“is anyone else talking right now?”)
If “busy”: wait; if “idle”: transmit
CD: Keep listening while transmitting
  If collision detected: retry at a later time
A
C
B
Don’t
transmit
Can collisions still occur?

## Slide 28: Example: Wi-Fi (802.11)
Most popular wireless LAN architecture
Access point
Wi-Fi router
Base station
Hotspot

## Slide 29: Example: Wi-Fi (802.11)
CSMA/CA Protocol
  Carrier Sense
  Multiple Access
  Collision Avoidance
    Channel reservations:
      Transmitter sends request-to-send (RTS)
      Receiver sends clear-to-send (CTS)
    Advantages:
      Nodes hearing RTS and/or CTS keep quiet
      If collision, only small RTS or CTS packets are lost

## Slide 30: Network Layer (Layer 3)
Dominant protocol: IP = Internet Protocol
Addressing and routing (sender & receiver IP address)
Uses 32 bit hierarchical address space with location information embedded in the structure
IPv4 address is usually expressed in dotted-decimal notation, e.g.:
128.100.11.56
Network ID
Host ID
4 bytes

## Slide 31: IPv4

## Slide 32: IPv6
IPv6 addresses are 128 bits long
16 bytes of IPv6 address are represented as a group of hexadecimal digits, separated by colons, e.g.:
2000:fdb8:0000:0000:0001:00ab:853c:39a1
Shorthand – leave out groups of zeros and leading zeros:
2000:fdb8:::1:ab:853c:39a1

## Slide 33: Network Protocols (“Protocol Stack”)
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Communication Network
Figure 2.6
Copyright ©2000 The McGraw Hill Companies

## Slide 34: Routers
Form backbone of the Internet
Use IP layer to identify source and destination of packets
Look up routing tables that determines “next hop”
Destination | Next Hop
147.39.21.X | 131.19.18.121
89.44.X.X | 131.19.22.119
203.21.X.X | 137.18.47.48

## Slide 35: Transport Layer (Layer 4)
UDP (User Datagram Protocol)
Adds more addressing: “ports”
  IP address tell you which computer
  Ports tell you which application on that computer
  Example: a web server “listens” to requests on port 80
  Web browser: http://www.google.com:80 = http://216.58.216.100:80
    “:80": optional
  Unreliable!
    Packets can get lost; packets can arrive out of order
Data
UDP Header

## Slide 36: Transport Layer
TCP (Transmission Control Protocol)
Reliable protocol!
Adds ports (just like UDP), but also provides:
  In-order delivery of packets (using sequence numbers)
  Reliable delivery: using acknowledgment (ACK) packets
  Flow control & congestion control:
    Allows receiver to slow down sender
    Allows “network” to slow down sender
Packet
ACK

## Slide 37: UDP vs TCP
TCP:
  typical choice of most applications
  do not want to lose data, out-of-order arrival, etc.
  email, web traffic, financial transactions, etc.
UDP:
  can be “faster”
    no flow/congestion control “slowing down” traffic
    no retransmissions
    good for “real-time” traffic
  out-of-order arrival: can also “reorder” at application level
  loss of data: can be acceptable
    missing frames in video/audio stream

## Slide 38: Upper Layers (Layers 5-7)
Session Layer
  Management of “sessions”
Presentation Layer
  Data translation, formatting, encryption, compression
Application Layer
  Interface between user applications and lower network services

## Slide 39: Example: Web Servers
HTTP
server
HTTP
client
Request
Response

## Slide 40: Example: Web Servers
HTTP
server
HTTP
client
TCP
TCP
GET 80, #
#, 80 STATUS
Port 80
Ephemeral
Port #

## Slide 41: Example: Web Servers
HTTP Request
TCP Header
Header contains source and destination port numbers
Header contains source and destination IP addresses; transport protocol type
IP Header
Header contains source and destination physical addresses; network protocol type
Frame Check Sequence
Ethernet Header

## Slide 42: BREAK