## Slide 1: Internet-of-Things (IoT)
Summer Engineering Program 2018
University of Notre Dame
LAB COMPONENT

## Slide 2: Assignment 4: MQTT
Task 1: Configure MQTT broker
Task 2: Write an MQTT publisher for your RPi; your publisher should periodically publish sensor data
Task 3: Write an MQTT subscriber for your RPi; your subscriber should activate an actuator
Task 4: Work in teams of 2-4 to build a complete IoT system that does something meaningful using at least 2 RPis, 1 sensor, 1 output device, and the MQTT broker (if PIR + LED only, max score is 90%; max score is 100% if at least one new sensor or output device)

## Slide 3: RPi Preparations for MQTT
sudo apt-get update
sudo apt-get install python-pip
pip install paho-mqtt

## Slide 4: Configure MQTT Broker
Sign up for account at: https://www.cloudmqtt.com/
Create new instance:
  Descriptive name
  Plan: free
  Location: doesn‘t matter much
  Tags: can ignore
Click instance to learn server name, username, password, and port number

## Slide 5: Backup Broker Information (If Needed)
fortuitous-butcher.cloudmqtt.com
User: smrpzowq
Password: ahxFJm2zWXJF
Port: 1883

## Slide 6: Set Up MQTTlens
Optional, but good for debugging
Install/start Chrome
Look for MQTTlens Google Chrome application
Establish a new connection: use server, username, password, port number
Choose a “topic“; subscribe to topic; publish to topic
Provides real-time feedback

## Slide 7: Using MQTT in Python Program
import paho.mqtt.client as mqtt
import time
import sys
#Create a client instance
client = mqtt.Client()
#Set username and password for broker
client.username_pw_set(username, pwd)
#Connect to broker
connect(host, port)
#Start client loop
client.loop_start()
...
#Disconnect (end of program)
client.disconnect()
client.loop_stop()

## Slide 8: Available Callbacks
client.on_log = on_log
client.on_connect = on_connect
client.on_disconnect = on_disconnect
client.on_subscribe = on_subscribe
client.on_unsubscribe = on_unsubscribe
client.on_publish = on_publish
client.on_message = on_message

## Slide 9: Callback Examples
def on_connect(client, userdata, flags, rc):
print("rc: " + str(rc))
def on_message(client, obj, msg):
print(msg.topic + " " + str(msg.qos) + " " + str(msg.payload))
def on_publish(client, obj, mid):
print("mid: " + str(mid))
def on_subscribe(client, obj, mid, granted_qos):
print("Subscribed: " + str(mid) + " " + str(granted_qos))
def on_log(client, obj, level, string):
print(string)

## Slide 10: Connection Establishment
connected = False
#initiate connection; in on_connect set connected to True (make sure „connected“ is a global variable)
while connected == False
time.sleep(1)

## Slide 11: MQTT Publish & Subscribe
client.subscribe(topic, quality)
client.publish(topic, sensordata)

## Slide 12: MQTT Program
import statements
callback functions
create client instance
set callback functions for client
connect to broker and start loop
wait until connection established
subscribe to topic(s) (if subscriber)
publish to topic(s) (if publisher)
if program ended, disconnect and stop loop

## Slide 13: MQTT Program
while (1):
try:
#if publisher:
mqttc.publish(topic, sensordata)
time.sleep(desired_sleep_period)
except KeyboardInterrupt:
client.disconnect()
sys.exit()